## Slide 1: Mechanical Ventilation
Dr. Zia Arshad
MD, FRCP (Edin.), FCCM, FIACM, MNAMS
Professor
Department of Anaestheiology & Critical Care
King George’s Medical University
Lucknow

## Slide 2
Indication
Mode
Variable
Initiation of mechanical ventilation
Goal
Monitoring
Ventilator alarms and there trouble shooting
Weaning from ventilator
Complication

## Slide 3: indication
For intubation
For ventilation
Respiratory failure
Neuromuscular disorder

## Slide 4: Modes
CMV
AC
SIMV
PRVC
PS
ASV,APRV

## Slide 5: variable
Respiratory rate
Tidal volume
PEEP
I:E Ratio
Pressure support
Trigger (Pressure/Flow)
Pressure limit

## Slide 6: Controlled Mandatory ventilation
All breaths are mandatory
Preset frequency, inspiratory time/Inspiratory flow
Pressure or volume control
Trigger: Time
Limit: Volume, flow or pressure
Cycle: Time, volume

## Slide 7: Volume vs. Pressure Control
Volume Preset
Set parameter is the tidal volume; airway pressure is variable
Constant tidal volume in the face of changing lung characteristics
Patient-ventilator asynchrony due to fixed flow rate
No leak compensation
Pressure Preset
Set parameter is airway pressure; tidal volume delivered is variable
Tidal volume varies with changes in lung characteristics
Flow will vary according to patient's demands
Compensates for leaks

## Slide 8: Assist control
Like CMV
Each additional assisted breath at prefixed tidal volume or pressureTrigger: ventilator or patient
Limit: Flow / volume or Pressure
Cycling: volume or time

## Slide 9: Synchronised intermittent mandatory ventilation
  Synchronised mandatory breaths with spontaneous breaths allowed in between
  Ventilator creates a time window around the scheduled delivery of mandatory breath
  If a patient effort is detected, it synchronises the machine breath with the patient’s inspiration
  If no patient effort is detected, it delivers a breath at the scheduled time

## Slide 10
Pressure
Flow
Volume
(L/min)
(cm H2O)
(ml)
Time (sec)
SIMV Mode
Spontaneous Breath

## Slide 11: Pressure Support
Completely spontaneous mode in which patient triggers each breath
On inspiration patient exposed to a preset pressure
Inspiration is terminated when the flow rate reaches a minimum level or % of peak flow
Trigger: Patient
Limit: Pressure
Cycling: flow

## Slide 12: Initiating Mechanical Ventilation
Check ventilator assembly: power connection, circuit connection, HME filter catheter mount, gas connections
Switch on ventilator, check on test lung
Begin Preoxygenation (aerosol precaution)
Watch for Hypotension
  Infuse Fluids
Start Mechanical Ventilation
  A/C:TV=350-450, RR=20-30, FIO2= 60-100%
  Peak Flow rate 40-60 l/min
  PEEP=5-10, I:E=1:2, Sens= -0.8 - 2

## Slide 13: GOAL
OXYGENATION GOAL: PaO255-80 mmHg or SpO2 88-95%
PLATEAU PRESSURE GOAL: ≤ 30 cm H2O
pH GOAL: 7.30-7.45
Acidosis Management: (pH < 7.30)
If pH 7.15-7.30: Increase RR until pH > 7.30 or PaCO2 < 25 (Maximum set RR = 35).
If pH < 7.15: Increase RR to 35.
If pH remains < 7.15, TV may be increased in 1 ml/kg steps until pH > 7.15 (Pplat target of 30 may be exceeded). (Max TV =8, Min TV=4 ml/kg)
Alkalosis Management: (pH > 7.45) Decrease vent rate if possible.

## Slide 14: Monitoring
Heart rate
SpO2
Respiratory rate
Pattern of respiration and signs of respiratory distress
Blood pressure
ETCO2
Expired tidal volume: equal to set tidal volume (leaks)
Peak pressure, Plateau pressure (< 30 mm Hg)

## Slide 15: Ventilator alarms and troubleshooting
Alarms | Priority | Causes | Steps
Electrical power/ gas delivery/ Battery | Highest | Disconnection of power supply or oxygen source | Connect the power or Oxygen source
Low airway pressure | High | Disconnection or volume leak, in appropriate alarm setting | Connect ventilator, check alarm setting
High airway pressure | High | Obstruction to flow, pneumothorax and other compliance problem (fluid overload/ abdominal hypertension) | Check for Ppeak and Pplat (diff <3-5) if both high: Compliance problem (pneumothorax etc) If Ppeak and Pplat (diff>3-5) : Resistance problem (tube/circuit block etc): suction/change tube, bronchodilator
Low Expired Vt | High | ETT cuff leak, Circuit leak, leak from HME filter, leak from ICD | Check/change ETT, Circuit, HME filter, ICD
High RR High PEEP | Moderate | Blocked tube/bronchoconstriction | Suction/bonchodilation

## Slide 16: Management of other problems
Hypoxemia: check for disconnection, Increase Fio2, Call for help, check for tube block, fluid overload, check air entry, patient ventilator asynchrony
DOPE:
D: Disconnection/ Dislodging
O: Obstruction,
P: Pneumothorax
E: Equipment failure
There may exist multiple problems

## Slide 17: Criteria for consideration for Weaning/discontinuation
Underlying disease stable or improving
PaO2 / FiO2 > 200
PEEP < 5-8 cmH2O
FiO2 < 0.5
Reliable respiratory drive
Stable CVS
  Minimal pressors or inotropes
  Absence of myocardial ischemia
Capable of initiating inspiratory effort

## Slide 18
Underlying condition has
Resolved or improved and there is no other condition mandating MV
Daily screening of RS function
Not Ready
Ready
MV and
Daily screening
SBT
T-piece or PSV
30min is enough
Tolerated
Not tolerated
Gradual Withdrawal
Once-daily T-piece
PSV
Weaning

## Slide 19: Complications of MV
Airway management related complications
Hypotension
Pneumothorax/Subcutaneous emphysema
Ventilator induced lung injury
Ventilator associated pneumonia

## Slide 20: Non invasive ventilation
Indication
Pre requisite
Contraindication
Variables
complications

## Slide 21: CARRY HOME MESSAGE
CoViD-19 patients usually present to ICU with ARDS.
For ventilating these patients Tidal volume (TV) should be calculated by 6 ml/kg PBW. (TVmax=8 ml/kg, TVmin=4 ml/kg)
Ventilating a patient with ARDS: Low TV, High RR, High PEEP and Plateau pressure < 30 cm H2O.
One should be aware of monitoring and troubleshooting of mechanical ventilator.
Patient should be initiated on Controlled or assist control mode of MV and once recovers can be weaned using spontaneous breathing trial.

## Slide 22
THANK YOU